## Slide 3: Light
Computer Vision
James Hays

## Slide 4: Projection: world coordinatesimage coordinates
Camera Center (0, 0, 0)
.
.
.
f
z
y
.
v’
u’
If X = 2, Y = 3, Z = 5, and f = 2 What are U and V?
3
5
-2
?
Notes: Being a little loose about coordinates vs lengths
u and v prime because they are in the same coordinate system as x, y, and z but in later slides u and v will be –u’ and –v’ because they are in their own coordinate system which is mirrored

## Slide 5: Interlude: why does this matter?

## Slide 6: Relating multiple views

## Slide 7
K
Slide Credit: Savarese
Projection matrix
Intrinsic Assumptions
Unit aspect ratio
Optical center at (0,0)
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
X
x
Notes: Work through equations for u and v on board

## Slide 8: Remove assumption: optical center at origin
Intrinsic Assumptions
Unit aspect ratio
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)

## Slide 9: Remove assumption: square pixels
Intrinsic Assumptions
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)

## Slide 10: Remove assumption: non-skewed pixels
Intrinsic Assumptions
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
Note: different books use different notation for parameters

## Slide 11: Oriented and Translated Camera
Ow
iw
kw
jw
t
R
X
x

## Slide 12: Allow camera translation
Intrinsic Assumptions
Extrinsic Assumptions
No rotation

## Slide 13: 3D Rotation of Points
Rotation around the coordinate axes, counter-clockwise:
p
p’
g
y
z
Slide Credit: Saverese

## Slide 14: Allow camera rotation

## Slide 15: Degrees of freedom
5
6
Notes: How many known points are needed to estimate this?

## Slide 16: Reminder: read your book
Lectures have assigned readings
Szeliski 2.1 and especially 2.1.5 cover the geometry of image formation

## Slide 17: Field of View (Zoom, focal length)

## Slide 18: Things to remember
Vanishing points and vanishing lines
Pinhole camera model and camera projection matrix
Homogeneous coordinates
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)

## Slide 19: Image Formation
Digital Camera
The Eye
Film

## Slide 20: A photon’s life choices
Absorption
Diffusion
Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
λ
light source
?

## Slide 21: A photon’s life choices
Absorption
Diffusion
Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
λ
light source

## Slide 22: A photon’s life choices
Absorption
Diffuse Reflection
Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
λ
light source

## Slide 23: A photon’s life choices
Absorption
Diffusion
Specular Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
λ
light source

## Slide 24: A photon’s life choices
Absorption
Diffusion
Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
λ
light source

## Slide 25: A photon’s life choices
Absorption
Diffusion
Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
λ
light source

## Slide 26: A photon’s life choices
Absorption
Diffusion
Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
λ1
light source
λ2

## Slide 27: A photon’s life choices
Absorption
Diffusion
Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
λ
light source

## Slide 28: A photon’s life choices
Absorption
Diffusion
Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
t=1
light source
t=n

## Slide 29: A photon’s life choices
Absorption
Diffusion
Reflection
Transparency
Refraction
Fluorescence
Subsurface scattering
Phosphorescence
Interreflection
λ
light source
(Specular Interreflection)

## Slide 30: Lambertian Reflectance
In computer vision, surfaces are often assumed to be ideal diffuse reflectors with no dependence on viewing direction.

## Slide 31: Digital camera
A digital camera replaces film with a sensor array
  Each cell in the array is light-sensitive diode that converts photons to electrons
  Two common types
    Charge Coupled Device (CCD)
    CMOS
  http://electronics.howstuffworks.com/digital-camera.htm
Slide by Steve Seitz

## Slide 32: Sensor Array
CMOS sensor

## Slide 33: Sampling and Quantization

## Slide 34: Interlace vs. progressive scan
http://www.axis.com/products/video/camera/progressive_scan.htm
Slide by Steve Seitz

## Slide 35: Progressive scan
http://www.axis.com/products/video/camera/progressive_scan.htm
Slide by Steve Seitz

## Slide 36: Interlace
http://www.axis.com/products/video/camera/progressive_scan.htm
Slide by Steve Seitz

## Slide 37: Rolling Shutter
Notes: http://en.wikipedia.org/wiki/Rolling_shutter
Even DSLRs have this problem.

## Slide 38: The Eye
The human eye is a camera!
  Iris - colored annulus with radial muscles
  Pupil - the hole (aperture) whose size is controlled by the iris
  What’s the “film”?
    photoreceptor cells (rods and cones) in the retina
Slide by Steve Seitz

## Slide 39: Aside: why do we care about human vision in this class?
We don’t, necessarily.

## Slide 40: Ornithopters

## Slide 41: Why do we care about human vision?
We don’t, necessarily.
But cameras necessarily imitate the frequency response of the human eye, so we should know that much.
Also, computer vision probably wouldn’t get as much scrutiny if biological vision (especially human vision) hadn’t proved that it was possible to make important judgements from 2d images.

## Slide 42: Does computer vision “understand” images?
"Can machines fly?" The answer is yes, because airplanes fly.
"Can machines swim?" The answer is no, because submarines don't swim.
"Can machines think?" Is this question like the first, or like the second?
Source: Norvig

## Slide 43: The Retina

## Slide 44: Retina up-close
Light
Notes: Tapetum lucidum

## Slide 45: What humans don’t have: tapetum lucidum
Human eyes can reflect a tiny bit and blood in the retina makes this reflection red.
Notes: Animals with Tapetum Lucidum also have RPE, just not in the same part of the eye.

## Slide 46
© Stephen E. Palmer, 2002
Cones
cone-shaped
less sensitive
operate in high light
color vision
Two types of light-sensitive receptors
Rods
rod-shaped
highly sensitive
operate at night
gray-scale vision

## Slide 47: Rod / Cone sensitivity

## Slide 48
© Stephen E. Palmer, 2002
Distribution of Rods and Cones
Night Sky: why are there more stars off-center? Averted vision: http://en.wikipedia.org/wiki/Averted_vision

## Slide 49: Wait, the blood vessels are in front of the photoreceptors??
https://www.youtube.com/watch?v=L_W-IXqoxHA
Notes: Yes, and you can see them!

## Slide 51: Eye Movements
Saccades
Can be consciously controlled. Related to perceptual attention.
200ms to initiation, 20 to 200ms to carry out. Large amplitude.
Microsaccades
Involuntary. Smaller amplitude. Especially evident during prolonged fixation. Function debated.
Ocular microtremor (OMT)
involuntary. high frequency (up to 80Hz), small amplitude.
Smooth pursuit – tracking an object

## Slide 52: Electromagnetic Spectrum
http://www.yorku.ca/eye/photopik.htm
Human Luminance Sensitivity Function
Notes: At least 3 spectral bands required (e.g. R,G,B)

## Slide 53
Why do we see light of these wavelengths?
© Stephen E. Palmer, 2002
…because that’s where the
Sun radiates EM energy
Visible Light
Notes: Because that’s where the Sun’s peak radiation was
Because the atmosphere is fairly transparent in that range
Because biology has many important markers in that range (but that’s because of the previous two reasons)

## Slide 54
The Physics of Light
Any patch of light can be completely described
physically by its spectrum: the number of photons
(per time unit) at each wavelength 400 - 700 nm.
© Stephen E. Palmer, 2002

## Slide 55
The Physics of Light
Some examples of the spectra of light sources
© Stephen E. Palmer, 2002

## Slide 56
The Physics of Light
Some examples of the reflectance spectra of surfaces
Wavelength (nm)
% Photons Reflected
Red
400 700
Yellow
400 700
Blue
400 700
Purple
400 700
© Stephen E. Palmer, 2002

## Slide 57
The Psychophysical Correspondence
There is no simple functional description for the perceived
color of all lights under all viewing conditions, but …...
A helpful constraint:
Consider only physical spectra with normal distributions
area
mean
variance
© Stephen E. Palmer, 2002

## Slide 58
The Psychophysical Correspondence
Mean
Hue
# Photons
Wavelength
© Stephen E. Palmer, 2002

## Slide 59
The Psychophysical Correspondence
Variance
Saturation
Wavelength
# Photons
© Stephen E. Palmer, 2002

## Slide 60
The Psychophysical Correspondence
Area
Brightness
# Photons
Wavelength
© Stephen E. Palmer, 2002

## Slide 61
© Stephen E. Palmer, 2002
Three kinds of cones:
Physiology of Color Vision
Why are M and L cones so close?
Why are there 3?

## Slide 62: Impossible Colors
Can you make the cones respond in ways that typical light spectra never would?
http://en.wikipedia.org/wiki/Impossible_colors

## Slide 63: Tetrachromatism
Most birds, and many other animals, have cones for ultraviolet light.
Some humans, mostly female, seem to have slight tetrachromatism.
Bird cone responses

## Slide 64: More Spectra
metamers
Notes: Metamerism can be illuminant based or observer based. Color blindness produced well known instances of metamerism.

## Slide 65: Color Sensing in Camera (RGB)
3-chip vs. 1-chip: quality vs. cost
Why more green?
http://www.cooldictionary.com/words/Bayer-filter.wikipedia
Why 3 colors?
Slide by Steve Seitz

## Slide 66: Practical Color Sensing: Bayer Grid
Estimate RGB at ‘G’ cells from neighboring values
Slide by Steve Seitz

## Slide 67: Color Image
R
G
B

## Slide 68: Images in Matlab
Images represented as a matrix
Suppose we have a NxM RGB image called “im”
  im(1,1,1) = top-left pixel value in R-channel
  im(y, x, b) = y pixels down, x pixels to right in the bth channel
  im(N, M, 3) = bottom-right pixel in B-channel
imread(filename) returns a uint8 image (values 0 to 255)
  Convert to double format (values 0 to 1) with im2double
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93
R
G
B
row
column

## Slide 69: Color spaces
How can we represent color?
http://en.wikipedia.org/wiki/File:RGB_illumination.jpg

## Slide 70: Color spaces: RGB
0,1,0
0,0,1
1,0,0
Image from: http://en.wikipedia.org/wiki/File:RGB_color_solid_cube.png
Some drawbacks
Strongly correlated channels
Non-perceptual
Default color space
R
(G=0,B=0)
G
(R=0,B=0)
B
(R=0,G=0)

## Slide 71: Color spaces: HSV
Intuitive color space
H
(S=1,V=1)
S
(H=1,V=1)
V
(H=1,S=0)

## Slide 72: Color spaces: YCbCr
Y
(Cb=0.5,Cr=0.5)
Cb
(Y=0.5,Cr=0.5)
Cr
(Y=0.5,Cb=05)
Y=0
Y=0.5
Y=1
Cb
Cr
Fast to compute, good for compression, used by TV

## Slide 73: Color spaces: L*a*b*
“Perceptually uniform”* color space
L
(a=0,b=0)
a
(L=65,b=0)
b
(L=65,a=0)

## Slide 74: If you had to choose, would you rather go without luminance or chrominance?

## Slide 75: If you had to choose, would you rather go without luminance or chrominance?

## Slide 76: Most information in intensity
Only color shown – constant intensity

## Slide 77: Most information in intensity
Only intensity shown – constant color

## Slide 78: Most information in intensity
Original image

## Slide 79: Back to grayscale intensity
0.92 | 0.93 | 0.94 | 0.97 | 0.62 | 0.37 | 0.85 | 0.97 | 0.93 | 0.92 | 0.99
0.95 | 0.89 | 0.82 | 0.89 | 0.56 | 0.31 | 0.75 | 0.92 | 0.81 | 0.95 | 0.91
0.89 | 0.72 | 0.51 | 0.55 | 0.51 | 0.42 | 0.57 | 0.41 | 0.49 | 0.91 | 0.92
0.96 | 0.95 | 0.88 | 0.94 | 0.56 | 0.46 | 0.91 | 0.87 | 0.90 | 0.97 | 0.95
0.71 | 0.81 | 0.81 | 0.87 | 0.57 | 0.37 | 0.80 | 0.88 | 0.89 | 0.79 | 0.85
0.49 | 0.62 | 0.60 | 0.58 | 0.50 | 0.60 | 0.58 | 0.50 | 0.61 | 0.45 | 0.33
0.86 | 0.84 | 0.74 | 0.58 | 0.51 | 0.39 | 0.73 | 0.92 | 0.91 | 0.49 | 0.74
0.96 | 0.67 | 0.54 | 0.85 | 0.48 | 0.37 | 0.88 | 0.90 | 0.94 | 0.82 | 0.93
0.69 | 0.49 | 0.56 | 0.66 | 0.43 | 0.42 | 0.77 | 0.73 | 0.71 | 0.90 | 0.99
0.79 | 0.73 | 0.90 | 0.67 | 0.33 | 0.61 | 0.69 | 0.79 | 0.73 | 0.93 | 0.97
0.91 | 0.94 | 0.89 | 0.49 | 0.41 | 0.78 | 0.78 | 0.77 | 0.89 | 0.99 | 0.93

## Slide 80: Next week
Convolution, Filtering, Image Pyramids, Frequencies, Project 1