## Slide 2
How is it that a 4MP image can be compressed to a few hundred KB without a noticeable change?
Compression

## Slide 3: Lossy Image Compression (JPEG)
Block-based Discrete Cosine Transform (DCT)
Slides: Efros

## Slide 4: Using DCT in JPEG
The first coefficient B(0,0) is the DC component, the average intensity
The top-left coeffs represent low frequencies, the bottom right – high frequencies

## Slide 5: Image compression using DCT
Quantize
  More coarsely for high frequencies (which also tend to have smaller values)
  Many quantized high frequency values will be zero
Encode
  Can decode with inverse dct
Quantization table
Filter responses
Quantized values

## Slide 6: JPEG Compression Summary
Convert image to YCrCb
Subsample color by factor of 2
  People have bad resolution for color
Split into blocks (8x8, typically), subtract 128
For each block
  Compute DCT coefficients
  Coarsely quantize
    Many high frequency components will become zero
  Encode (with run length encoding and then Huffman coding for leftovers)
http://en.wikipedia.org/wiki/YCbCr
http://en.wikipedia.org/wiki/JPEG

## Slide 7: Lossless compression (PNG)
Predict that a pixel’s value based on its upper-left neighborhood
Store difference of predicted and actual value
Pkzip it (DEFLATE algorithm)

## Slide 8
Why do we get different, distance-dependent interpretations of hybrid images?
?

## Slide 9: Application: Hybrid Images
A. Oliva, A. Torralba, P.G. Schyns, “Hybrid Images,” SIGGRAPH 2006

## Slide 10: Clues from Human Perception
Early processing in humans filters for various orientations and scales of frequency
Perceptual cues in the mid-high frequencies dominate perception
When we see an image from far away, we are effectively subsampling it
Early Visual Processing: Multi-scale edge and blob filters

## Slide 11: Campbell-Robson contrast sensitivity curve

## Slide 12: Hybrid Image in FFT
Hybrid Image
Low-passed Image
High-passed Image

## Slide 13
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Credit: S. Seitz
Review: Image filtering
1
1
1
1
1
1
1
1
1
Notes: ones, divide by 9

## Slide 14
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 15
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Image filtering
1
1
1
1
1
1
1
1
1
Credit: S. Seitz
Notes: ones, divide by 9

## Slide 16: Filtering in spatial domain
-1
0
1
-2
0
2
-1
0
1
*
=

## Slide 17: Filtering in frequency domain
FFT
FFT
Inverse FFT
=

## Slide 18: Review of Filtering
Filtering in spatial domain
  Slide filter over image and take dot product at each position
  Remember linearity (for linear filters)
  Examples
    1D: [-1 0 1], [0 0 0 0 0.5 1 1 1 0.5 0 0 0]
    1D: [0.25 0.5 0.25], [0 0 0 0 0.5 1 1 1 0.5 0 0 0]
    2D: [1 0 0 ; 0 2 0 ; 0 0 1]/4

## Slide 19: Review of Filtering
Filtering in frequency domain
  Can be faster than filtering in spatial domain (for large filters)
  Can help understand effect of filter
  Algorithm:
    Convert image and filter to fft (fft2 in matlab)
    Pointwise-multiply ffts
    Convert result to spatial domain with ifft2

## Slide 20: Review of Filtering
Linear filters for basic processing
  Edge filter (high-pass)
  Gaussian filter (low-pass)
FFT of Gaussian
[-1 1]
FFT of Gradient Filter
Gaussian

## Slide 21: Review of Filtering
Derivative of Gaussian

## Slide 22: Review of Last 3 Days
Applications of filters
  Template matching (SSD or Normxcorr2)
    SSD can be done with linear filters, is sensitive to overall intensity
  Gaussian pyramid
    Coarse-to-fine search, multi-scale detection
  Laplacian pyramid
    Teases apart different frequency bands while keeping spatial information
    Can be used for compositing in graphics
  Downsampling
    Need to sufficiently low-pass before downsampling

## Slide 23: Things to Remember
Sometimes it makes sense to think of images and filtering in the frequency domain
  Fourier analysis
Can be faster to filter using FFT for large images (N logN vs. N2 for auto-correlation)
Images are mostly smooth
  Basis for compression
Remember to low-pass before sampling

## Slide 24
The blue and green colors are actually the same

## Slide 25
http://blogs.discovermagazine.com/badastronomy/2009/06/24/the-blue-and-the-green/

## Slide 26: Previous Lectures
We’ve now touched on the first three chapters of Szeliski.
  1. Introduction
  2. Image Formation
  3. Image Processing
Now we’re moving on to
  4. Feature Detection and Matching
  Multiple views and motion (7, 8, 11)

## Slide 27: Edge / Boundary Detection
Computer Vision
James Hays
Many slides from Lana Lazebnik, Steve Seitz, David Forsyth, David Lowe, Fei-Fei Li, and Derek Hoiem
Szeliski 4.2

## Slide 28: Edge detection
Goal: Identify sudden changes (discontinuities) in an image
  Intuitively, most semantic and shape information from the image can be encoded in the edges
  More compact than pixels
Ideal: artist’s line drawing (but artist is also using object-level knowledge)
Source: D. Lowe

## Slide 29: Why do we care about edges?
Extract information, recognize objects
Recover geometry and viewpoint
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)

## Slide 30: Origin of Edges
Edges are caused by a variety of factors
depth discontinuity
surface color discontinuity
illumination discontinuity
surface normal discontinuity
Source: Steve Seitz

## Slide 31: Closeup of edges
Source: D. Hoiem

## Slide 32: Closeup of edges
Source: D. Hoiem

## Slide 33: Closeup of edges
Source: D. Hoiem

## Slide 34: Closeup of edges
Source: D. Hoiem

## Slide 35: Characterizing edges
An edge is a place of rapid change in the image intensity function
image
intensity function (along horizontal scanline)
first derivative
edges correspond to extrema of derivative

## Slide 36: Intensity profile
Source: D. Hoiem

## Slide 37: With a little Gaussian noise
Gradient
Source: D. Hoiem

## Slide 38: Effects of noise
Consider a single row or column of the image
  Plotting intensity as a function of position gives a signal
Where is the edge?
Source: S. Seitz
Notes: How to fix?

## Slide 39: Effects of noise
Difference filters respond strongly to noise
  Image noise results in pixels that look very different from their neighbors
  Generally, the larger the noise the stronger the response
What can we do about it?
Source: D. Forsyth

## Slide 40: Solution: smooth first
To find edges, look for peaks in
f
g
f * g
Source: S. Seitz

## Slide 41: Derivative theorem of convolution
Differentiation is convolution, and convolution is associative:
This saves us one operation:
f
Source: S. Seitz

## Slide 42: Derivative of Gaussian filter
* [1 -1] =
Notes: Is this filter separable?

## Slide 43: Tradeoff between smoothing and localization
Smoothed derivative removes noise, but blurs edge. Also finds edges at different “scales”.
1 pixel
3 pixels
7 pixels
Source: D. Forsyth

## Slide 44: Implementation issues
The gradient magnitude is large along a thick “trail” or “ridge,” so how do we identify the actual edge points?
How do we link the edge points to form curves?
Source: D. Forsyth
Notes: Figures show gradient magnitude of zebra at two different scales

## Slide 45: Designing an edge detector
Criteria for a good edge detector:
  Good detection: the optimal detector should find all real edges, ignoring noise or other artifacts
  Good localization
    the edges detected must be as close as possible to the true edges
    the detector must return one point only for each true edge point
Cues of edge detection
  Differences in color, intensity, or texture across the boundary
  Continuity and closure
  High-level knowledge
Source: L. Fei-Fei

## Slide 46: Canny edge detector
This is probably the most widely used edge detector in computer vision
Theoretical model: step-edges corrupted by additive Gaussian noise
Canny has shown that the first derivative of the Gaussian closely approximates the operator that optimizes the product of signal-to-noise ratio and localization
J. Canny, A Computational Approach To Edge Detection, IEEE Trans. Pattern Analysis and Machine Intelligence, 8:679-714, 1986.
Source: L. Fei-Fei
22,000 citations!

## Slide 47: Note about Matlab’s Canny detector
Small errors in implementation
  Gaussian function not properly normalized
  First filters with a Gaussian, then a difference of Gaussian (equivalent to filtering with a larger Gaussian and taking difference)

## Slide 48: Example
original image (Lena)

## Slide 49: Derivative of Gaussian filter
x-direction
y-direction

## Slide 50: Compute Gradients (DoG)
X-Derivative of Gaussian
Y-Derivative of Gaussian
Gradient Magnitude

## Slide 51: Get Orientation at Each Pixel
Threshold at minimum level
Get orientation
theta = atan2(gy, gx)

## Slide 52: Non-maximum suppression for each orientation
At q, we have a maximum if the value is larger than those at both p and at r. Interpolate to get these values.
Source: D. Forsyth

## Slide 53: Edge linking
Assume the marked point is an edge point. Then we construct the tangent to the edge curve (which is normal to the gradient at that point) and use this to predict the next points (here either r or s).
Source: D. Forsyth

## Slide 54: Sidebar: Bilinear Interpolation
http://en.wikipedia.org/wiki/Bilinear_interpolation

## Slide 55: Sidebar: Interpolation options
imx2 = imresize(im, 2, interpolation_type)
‘nearest’
  Copy value from nearest known
  Very fast but creates blocky edges
‘bilinear’
  Weighted average from four nearest known pixels
  Fast and reasonable results
‘bicubic’ (default)
  Non-linear smoothing over larger area (4x4)
  Slower, visually appealing, may create negative pixel values
Examples from http://en.wikipedia.org/wiki/Bicubic_interpolation

## Slide 56: Before Non-max Suppression

## Slide 57: After non-max suppression

## Slide 58: Before Non-max Suppression

## Slide 59: After non-max suppression

## Slide 60: Hysteresis thresholding
Threshold at low/high levels to get weak/strong edge pixels
Do connected components, starting from strong edge pixels

## Slide 61: Hysteresis thresholding
Check that maximum value of gradient value is sufficiently large
  drop-outs? use hysteresis
    use a high threshold to start edge curves and a low threshold to continue them.
Source: S. Seitz

## Slide 62: Final Canny Edges

## Slide 63: Canny edge detector
Filter image with x, y derivatives of Gaussian
Find magnitude and orientation of gradient
Non-maximum suppression:
  Thin multi-pixel wide “ridges” down to single pixel width
Thresholding and linking (hysteresis):
  Define two thresholds: low and high
  Use the high threshold to start edge curves and the low threshold to continue them
MATLAB: edge(image, ‘canny’)
Source: D. Lowe, L. Fei-Fei

## Slide 64: Effect of  (Gaussian kernel spread/size)
Canny with
Canny with
original
The choice of  depends on desired behavior
  large  detects large scale edges
  small  detects fine features
Source: S. Seitz

## Slide 65: Where do humans see boundaries?
Berkeley segmentation database: http://www.eecs.berkeley.edu/Research/Projects/CS/vision/grouping/segbench/
image
human segmentation
gradient magnitude

## Slide 66: Building Visual Dictionaries
Sample patches from a database
  E.g., 128 dimensional SIFT vectors
Cluster the patches
  Cluster centers are the dictionary
Assign a codeword (number) to each new patch, according to the nearest cluster

## Slide 67: pB boundary detector
Figure from Fowlkes
Martin, Fowlkes, Malik 2004: Learning to Detect Natural Boundaries…
http://www.eecs.berkeley.edu/Research/Projects/CS/vision/grouping/papers/mfm-pami-boundary.pdf

## Slide 68: pB Boundary Detector
Figure from Fowlkes

## Slide 69
Brightness
Color
Texture
Combined
Human

## Slide 70: Results
Human (0.95)
Pb (0.88)

## Slide 71: Results
Human
Pb
Human (0.96)
Global Pb
Pb (0.88)

## Slide 72
Human (0.95)
Pb (0.63)

## Slide 73
Human (0.90)
Pb (0.35)
For more: http://www.eecs.berkeley.edu/Research/Projects/CS/vision/bsds/bench/html/108082-color.html

## Slide 74: Global pB boundary detector
Figure from Fowlkes

## Slide 75: 45 years of boundary detection
Source: Arbelaez, Maire, Fowlkes, and Malik. TPAMI 2011 (pdf)

## Slide 76: State of edge detection
Local edge detection works well
  But many false positives from illumination and texture edges
Some methods to take into account longer contours, but could probably do better
Modern methods that actually “learn” from data.
Poor use of object and high-level information

## Slide 77: Style and abstraction in portrait sketching, Berger et al. SIGGRAPH 2013
Learn from artist’s strokes so that edges are more likely in certain parts of the face.