## Slide 1
Dynamic Reconfiguration
Dynamic selection of handler functionality:
currently through use of parameterizable handlers or by selecting from a set of existing handlers
assessing possibilities for runtime deployment of new codes
Admission control:
monitor use of resources such as headroom
consider both IXP- and host-side deployment
SPLITS Overview
Stream Handler - lightweight computational unit executed on the ANP which operates on both, packet header and payload data
SPLITS – Software architecture for Programmable LIghtweighT Stream handlers
  enables developers to dynamically deploy and configure service functionality onto attached network processors so as to best utilize the combined host/ANP resources
  implemented for standard Linux kernels and ANPs based on the Intel IXP network processors.
Objectives
Utilize programmable network processors in large scale distributed applications to:
attain improvements in end-user application performance,
more efficiently utilize host system capacity,
offer to applications new services at no additional performance overheads perceived by end users.
Map application- and middleware-level services across hosts and their attached NPs, thereby attaining integrated host-attached NP (ANP) systems
Host - Attached NP node: integrated platforms, building block in overlay networks, interactive grids, p2p systems, cluster servers…
Applications: commercial (OIS), scientific (RT collaborations), dynamic web applications (delivery of camera-captured data;
Services: application-level filtering, mirroring, stream differentiation, format translation, downsampling…
sample services implemented with stream handlers and SPLITS
Rx
SH
SH
SH
Tx
Control Mgt
Data
Mgt
Control Data
Data Buffers
resource state
ANP-HOST
INTERFACE
HOST
ANP
Resource Monitor
Admission Control
Application
h
h
Summary of Results:
Variety of application-level services can be efficiently implemented
Computationally intensive services such as image cropping for OpenGl graphics serves can be supported on the IXP NP at rates reaching 3.75Gbps;
Value-added services, such as format translation for XML-based applications, can be added at no additional cost perceived by end user;
Results indicate the importance of cooperative host/ANP processing for complex services where handlers are simultaneously deployed on the ANP and the host;
Performance gains stem from network-near execution of stream handlers, load reduction on the host system CPU and memory infrastructure, and the flexibility with which stream handlers can be mapped across host/ANP boundaries
Receive
Transmit
Access
user
kernel
protocol plane
host
ANP
from network
to network
Data Path through host/ANP.
Application- and middleware-level services are implemented as compositions of stream handlers simultaneously deployed at multiple points along the packets’ datapath through the integrated host/ANP nodes:
  on the ANP, embedded with packet receipt and transmission,
  on the ANP, after the application-level message has been assembled in ANP memory,
  or at the host kernel or user level
Application-level Services on Attached Network Processors
Ada Gavrilovska, Karsten Schwan,
Austen Mcdonald, Hailemelekot Seifu, Ola Nordstrom
Accessing application-level data:
efficient protocol for fragmentation and reassembly of application-level messages (RUDP)
use of portable binary data format descriptors (PBIO)
data format translation on the IXP for
XML-based applications